## Slide 1
1 / 8
Design and Simulation of a Smart Parking Slot Availability and Entry Control System Using Combinational Logic
Digital Logic Design and Logisim Simulation
TEAM MEMBERS
2620030600 – JETHENDRA VARDHAN
2620030602 – LAXMI PRAGYA
2620030606 – VEDA CHANDRA
2620030636 – CHANDRA PAUL
2620030675 – SRIKRISHNA
COMBINATIONAL LOGIC
ENTRY GATE
S1
S2
S3
S4
PARKING SLOTS + SENSORS + GATE + LOGIC

## Slide 2
Problem Statement and Proposed System
2 / 8
PROBLEM STATEMENT
Manual parking causes waiting and congestion
Drivers need to know if slots are available
Each slot’s status must be detected
Available slots must be identified
Entry only when parking space is available
Digital logic can automate these decisions
PROPOSED SOLUTION
A combinational-logic parking system that turns sensor inputs into four outputs:
Available-slot information
Occupancy status
Selected slot information
Entry-control decision
Parking Sensors
Encoder / Decoder
Multiplexer
Comparator + Logic Gates
Availability / Entry Decision
Gate Control

## Slide 3
Combinational Logic and Parking Inputs
3 / 8
COMBINATIONAL LOGIC
Output depends only on present input values
No memory element is required
Logic gates implement the decisions
Suited to real-time parking decisions
PARKING INPUTS
S1, S2, S3, S4 → slot sensors
V → vehicle detected at entrance
0 = Available / OFF
1 = Occupied / ON
Y = f(S1, S2, S3, S4)
S1
1
S2
0
S3
1
S4
1
AND
FULL
AVAILABLE
FULL = S1·S2·S3·S4 AVAILABLE = FULL′
NOT: Y = A′
AND
AND: Y = A·B
OR
OR: Y = A + B

## Slide 4
Multiplexer: Parking-Slot Selection
4 / 8
SEL1
1
SEL0
0
S1
0
AND
S2
1
AND
S3
1
AND
S4
0
AND
OR
Y
SEL = 10 → Y = S3 = 1
MUX selects one of four slot inputs
SEL1 SEL0 choose the slot monitored
Many signals → one output Y
SEL1 SEL0 | Selected Input
0 0 | S1
0 1 | S2
1 0 | S3
1 1 | S4
Y = S1·SEL1′·SEL0′ + S2·SEL1′·SEL0
+ S3·SEL1·SEL0′ + S4·SEL1·SEL0
4:1 MUX gate-level circuit

## Slide 5
Decoder: Parking-Slot Identification
5 / 8
A
0
B
1
AND
D0 (Slot 1)
AND
D1 (Slot 2)
AND
D2 (Slot 3)
AND
D3 (Slot 4)
A=0, B=1 → D1 = 1
Binary input → one active output
2-to-4: A, B select D0–D3
Each output = one parking slot
A | B | Active
0 | 0 | D0
0 | 1 | D1
1 | 0 | D2
1 | 1 | D3
D0 = A′B′ D1 = A′B
D2 = AB′ D3 = AB
2-to-4 decoder: NOT + AND gates

## Slide 6
Priority Encoder: Available Slot Identification
6 / 8
P4
1
P3
0
P2
0
P1
0
AND
OR
OR
Y1
Y0
(P1 only → 00)
P4 = 1 → Y1 Y0 = 11
Encoder: active input → binary code
Highest priority wins: P4>P3>P2>P1
Selects which slot to assign
P4 | P3 | P2 | P1 | Y1Y0
1 | X | X | X | 11
0 | 1 | X | X | 10
0 | 0 | 1 | X | 01
0 | 0 | 0 | 1 | 00
0 | 0 | 0 | 0 | 00/Inv.
X = don’t care
Y1 = P4 + P3
Y0 = P4 + P3′·P2

## Slide 7
Comparator and Complete Parking Control Circuit
7 / 8
PART A — COMPARATOR
Compares two binary values
Outputs: A>B, A=B, A<B
Available count vs required capacity
Available Count (A)
Required Capacity (B)
COMPARATOR
A>B
A=B
A<B
PART B — COMPLETE WORKING LOGIC
SENSORS
S1–S4
ENCODER
free-slot code
MUX
selected status
DECODER
slot position
COMPARATOR
+ LOGIC
count > 0
AVAILABLE
FULL
AND
V
1
GATE OPEN
G = V · A
V = vehicle A = parking available G = gate open
G=V·A

## Slide 8
Conclusion
8 / 8
Smart parking demonstrates a practical application of combinational logic
Parking sensors provide the system inputs
Multiplexer performs signal selection
Decoder identifies the selected parking position
Encoder / Priority Encoder converts parking information into binary form
Comparator and logic gates support the final parking decision
The complete system can be designed and verified using Logisim
Digital logic can solve an automated parking-control problem
THANK YOU
PARKING
SENSORS
ENCODER
MUX
DECODER
LOGIC